## Slide 1: Firewall Management and Troubleshooting Tutorial
© Copyright 1997-98 WITSEC Inc. All rights reserved.
Distributed under license by WITSEC Inc.

## Slide 2: Firewall Management and Troubleshooting
Topics within Tutorial
  DNS
  Mail
  Mail and DNS Relationship
  Routing
  Subnetting
  VPNs
  Authentication

## Slide 3: Firewall Management and Troubleshooting
Topics within Material (cont.)
  Trust Relationships
  Cabling
  Filtering Rules
  Netacls
  System Logging

## Slide 4: Firewall Management and Troubleshooting
Topics with Tutorial (continued)
  Backups
  Indiscriminate use of generic proxies
  Operating System Goodies
  The fine print from the vendor
  Internal network and its protocol suite
  Security Administration Procedures

## Slide 5: Firewall Management and Troubleshooting
Network and Security Policy
System Architecture
Internet Security Reviews
The Future
Evaluation
Vocabulary and Acronyms
Additional Information

## Slide 6: Purpose
Observations and research of common problems in firewall implementations and management
Presentation scope rarely covers details concerning firewall integrations into an Enterprise Network.
Presentations exist for planners and managers but none for the actual implementers.

## Slide 7: Purpose
Provide common trouble shooting techniques for uncommon occurrences.
Remove mystery of firewall systems.
Provide a reference list of solutions.

## Slide 8: Purpose
Examine and discuss services which are needed to integrate in order to have a well running firewall system.
DNS, Sendmail, Routing, Filter Rules, and System logging

## Slide 9: Understanding Selection of Product/Vendor
It all begins with a security policy :
  What sort of controls does you policy specify?
  What sort of authentication is required?
  What about data integrity?
  What about throughput vs security? Which is more important?
  Ease of use?
  Availability

## Slide 10: Understanding Selection of Product/Vendor
It all begins with a policy (continued):
  Escalation procedures
  Backups and reporting
  Who is trusted?
  Which services?

## Slide 11: Wrong Product for the Job
Bought a multi-homed proxy server instead of a router based solution.
  Proxy servers were designed for security over throughput.
  Proxy servers can support multiple interfaces but they were not designed to do it.

## Slide 12: Wrong Product for the Job
Put in packet filtering rules on an application gateway firewall.
  Punching holes into a proxy server firewall to allow for less secure UDP traffic.

## Slide 13: DNS
Configuring DNS is not a difficult thing to do. Most commercial firewalls even offer a basic DNS configuration. However, when DNS is not properly configured users become quite irate. DNS problems have a way of masquerading as other larger problems.

## Slide 14: DNS
Common DNS problems
  Misplaced SOA
  Secondary Zone Exchange
    Unsensible secondary exchanges
    Non existent secondary servers
  Primary Zone problems
    Trailing “.” syndrome
    Null zone
    Improper zone configurations
    Missing reverse zone records

## Slide 15: DNS
Common DNS problems (cont.)
  Fake root.cache
  Forgetting to enter DMZ hosts into internal nameserver
  Failure to properly delegate sub-domains
  Failure with the InterNIC
    Payment
    New registration
    Modify existing registration

## Slide 16: DNS
Common DNS problems (cont.)
  Miscellaneous
    Wildcard Syndrome
    Bogus domain
    Client problems
      Using the wrong NS
      Improper domain specification

## Slide 17: DNS
Misplaced Start of Authority record
  Problem: The SOA record is not available to serve out zone information on the internet. Usually a firewall was put in front of the Primary Nameserver
  Symptoms: Unable to receive mail. Slow responses. Also unable to receive traffic from hosts outside your domain on your servers unless they specify the IP address. (Note: Don’t confuse with routing problems)

## Slide 18: DNS
Misplaced Start of Authority record
  Solution: Try registering with the InterNIC.
    Some sites make the firewall the registered SOA for their zone.
    Other sites, make the firewall’s external interface address the IP address of the old nameserver. (No need to modify registration then).
    Some sites let the ISP do the DNS management for them and run a caching NS on the firewall.

## Slide 19: DNS
Secondary Zone Info
  Unsensible secondary zone transfers
    Problem: Attempting to pass zone info through the firewall (especially when DNS hiding) to the ISP
    Symptoms: Security Alerts on the firewall from the internal nameserver.
    Solution: Have firewall exchange zone info with the ISP.

## Slide 20: DNS
Secondary Zone Info
  Non existent domain
    Problem: Secondary zone exchanges are not performed and error messages appear when the zone exchanges are set to be performed.
    Symptoms: Error messages in logs. Secondary nameserver has no info on the domain that it is exchanging records with.
    Solution: Check syntax of secondary line in /etc/named.boot and verify destination host has DNS running.

## Slide 21: DNS
Zone problems
  Trailing “.”syndrome
    Problem: a misplaced “.” results in the host or domain not being properly identified. Depending on where the “.” was misplaced.
    Symptoms: unable to properly resolve names for the host/domain. If the “.” is missing from the domain the domain is doubly appended on mail resulting in the inability to receive mail
    Solution: when defining domain don’t forget “.” when identifying hosts w/ FQDN dont forget “.”

## Slide 22: DNS
Zone problems
  Null zone
    Problem: Attempt to perform DNS query and zone transfer and zone info is missing; thus, a 0 value is returned.
    Symptom: Null info is being pushed out to the internet users are unable to web (or other services) in or out.
    Solution: Ensure DNS is properly entered. If ISP is managing DNS ensure correct values exist (use

## Slide 23: DNS
Zone problems
  Null zone
    Solution(continued): nslookup or dig). If you are exchanging secondary between firewall and ISP ensure port 53 is enabled for both TCP and UDP.
    Note: If you are exchanging secondary info with the primary at the ISP make sure to provide info only on hosts that you want to show.

## Slide 24: DNS
Zone problems
  Improper zone configurations
    Problem: Domain is either missing records, or they are incorrect. See trailing “.” syndrome.
    Symptom: Mail not working, unable to resolve hosts within own domain. Unable to locate hosts in own domain (not to be confused with routing problems), especially when referencing hosts by name. Able to perform operations when hosts are referenced by IP address.

## Slide 25: DNS
Zone problems:
  Improper zone configurations (continued):
    Solution: Fix DNS zone files and test thoroughly using nslookup or dig.

## Slide 26: DNS
Zone problems
  Missing reverse zone records
    Problem: Servers attempt to perform a reverse lookup on a host and will at best register an unknown but will most often perform a timeout.
    Symptom: Slow server response due to DNS timeout.
    Solution: Make sure forward and reverse records are present. If ISP is providing nameservice make sure that ISP has both IN A and IN PTR records for the firewall.

## Slide 27: DNS
Common DNS problems
  The “fake” root.cache
    Problem: Results from running DNS usually before internet connection so System Administrator entered a “fake” record on the internal nameserver in the root.cache to speed up the response.
    Symptom: Unable to resolve names outside of own domain. Appearance of “forwarders record” not working.

## Slide 28: DNS
Common DNS problems
  The fake “root.cache” (continued)
    Solution: Get rid of “fake” record, on internal ns root.cache. Either replace with firewall nameserver or use the real nameserver.

## Slide 29: DNS
Failure to enter DMZ hosts into the internal nameserver:
  Problem: DMZ hosts were defined in the external nameserver, but not the internal nameserver
  Symptoms: External users can get to DMZ hosts like the web server, but internal users can not.
  Solution: Add DMZ hosts records in zone files.

## Slide 30: DNS
Failure to properly delegate sub-domains
  Problem: Parent domain does not delegate sub-domain and has a host with the name of a sub-domain.
  Symptom: Problems with mail and other services.

## Slide 31: DNS
Failure to properly delegate sub-domains (continued):
  Solution: Independent registration of the domain with the InterNIC can sometimes help. But if a parent does not wish to delegate, the child domain could be in for a rough time since the parent is the root.

## Slide 32: DNS
Failure with the InterNIC
  Problem: whois domain name returns status of: HOLD - Dropped from DNS - in 60 day window.
  Symptom: DNS fails entirely.
  Solution: Until annual domain name renewal is paid. (after initial two-year period) : $50 Covers updates to domain name's database record.

## Slide 33: DNS
Updates that are not covered by this fee are: changes in the domain name itself, transfers of the domain name to another party, changes in the Organization beyond a change of the Organization's name. These actions are not considered updates and require a new registration to be processed.
    In essence pay your DNS Renewal FEE when it is due!!!

## Slide 34: DNS Registration Fees from the Internic
New Registration
  Domain name registration (.com, .org, and .net): $100.
  Covers initial registration and updates to the domain name's database record for a period of two years. Updates that are not covered by this fee are: changes to the domain name itself; transfers of the domain name to another party; changes in the Organization's information that in effect represent a transfer of the domain name to another legal entity.
  These actions are not considered updates and require a new registration to be processed, which will be subject to the $100 (US) new registration fee.

## Slide 35: Status Codes from Internic
Status codes
  PAID - Invoice paid.
  RENEW - 60 day renewal sent (Not yet invoiced).
  OPEN - Invoice sent.
  15DAY - 15 day notice sent.
  HOLD - Dropped from DNS - in 60 day window.
  REMOVED - Removed from the database for non-payment.
  WHOA - pending
Please be aware that there is typically a 24-hour delay between when your payment is processed and when your payment is reflected is reflected in the INTERNIC database

## Slide 36: Terms
New registration -Net 30 days. If payment is not received by the due date, the domain name is subject to deactivation and deletion.
Renewal -Net 30 days. If payment is not received by the due date (anniversary date), the domain name is subject to deactivation and deletion.

## Slide 37: DNS
Miscellaneous
  Bogus domains
    Problem: DNS “hiding” does not mean having a non-standard domain. Such as balt.pw instead of balt.pw.com
    Symptom: Unable to resolve queries outside of domain
    Solution: Aliases are your friend. Try aliasing the zone to a legit zone. Of course the better choice would be to avoid doing something like this in the first place.

## Slide 38: DNS
Some Trouble Shooting Tricks for DNS
  nslookup
    Resolve off of self to verify your nameserver works
      Test for all of the following record types: IN A, IN PTR, and IN MX
    Resolve off of another site outside of your domain to verify what everyone else sees
      Test for all of the following record types: SOA, IN MX, IN NS, IN A, and IN PTR

## Slide 39: DNS
Some Trouble Shooting Tricks for DNS (continued)
  dig <type> <domain>
    Type = DNS record type
    Domain = the domain that you are testing

## Slide 40: Electronic Mail
SMTP: What is it?
SMTP <> Mailhub
Paid for SMTP Gateway but got toaster oven
The Mail Consultant is the Expert
Home Grown

## Slide 41: Electronic Mail
Naked Sendmail
Spam alert
Boom (Mail Bombs)
FQDN
Internal Mailhub does not recognize own domain

## Slide 42: Electronic Mail
SMTP : What is it?
  Simple Mail Transfer Protocol
  Protocol not Software
  Good software should be compliant with the protocol (RFC 822)

## Slide 43: Electronic Mail
SMTP <> Mailhub
  Not all mail wrappers are store and forward
  Packet filtering firewalls need to address where the actual mailhub runs.
  MTA is only MTA not necessarily SMTP compliant

## Slide 44: Electronic Mail
Paid for SMTP Gateway, got toaster oven
  Problem - Internal mailhub is not SMTP compliant.
  Symptom - Mail keeps bouncing off of the internal mailhub.
  Solution - Telnet to port 25 of the internal mailhub to determine what it is expecting. If it is expecting something unlike SMTP you will be writing a mailer in your sendmail.cf file.

## Slide 45: Electronic Mail
Mail Consultant is the Expert
  Problem - The company paid for a mail consultant who is very knowledgeable on the mailhub but may lack the knowledge on the overall network
  Symptom - You guessed it … undeliverable mail.
  Solution - More often than not the internal hub does not recognize its own domain. Re-write ruleset 0 in sendmail.cf

## Slide 46: Electronic Mail
Home Grown
  Problem: Not necessarily a technical problem unless not SMTP compliant. Many companies have a mail person who wrote many sendmail rules (or even mailers) and these may not scale well for future growth.
  Symptoms: Mailhub may have outgrown use, so periodic failures or a total mail failure occurs.

## Slide 47: Electronic Mail
Home Grown:
  Solution: Re-evaluate and select the best fit commercial product available. Run a mail wrapper on your firewall (smap/smapd) and have it handoff mail to the internal product. Buy a good mail book (“Sendmail” or “Sendmail: Theory and Practice”).

## Slide 48: Electronic Mail
Naked Sendmail
  Problem: Mail on the mailhub does not work at all, or worse yet works inconsistently.
  Symptoms: In house staff can not support “out of the box” sendmail.
  Solution(1): Ensure that the mail package that you select can be support by the in house staff and can be easily configured to your site needs.

## Slide 49: Electronic Mail
Naked Sendmail (continued):
  Solution (2): By telnetting to port 25 you can determine what the internal mailhub is expecting and in what format (recipient ok), based on that you can write a mailer into sendmail complete with it’s own rulesets.

## Slide 50: Electronic Mail
SPAM Alert
  Problem: - Users use your mailhub as a site to launch mail to spam other users.
  Symptom: - Annoying calls and mail asking you to stop spamming other sites
  Solution: - There are several but the easiest; therefore, our recommendation is to run smap/smapd on your firewall. Modify the netperm-table to have smap write to a different

## Slide 51: Electronic Mail
SPAM Alert (continued)
  Solution (continued): - directory than the one that smapd “pulls”. Write a script to check for connections from the firewall to outside. When the script detects naughty behavior log it and write the message to /dev/null (or some other place if you are saving them). Move the file to /var/spool/smap when finished.

## Slide 52: Electronic Mail
Boom (Mail Bombs)
  Problem: Mail can not handle oversized messages and they are sent to all@your.domain
  Symptoms: Dead mail processes, “connection reset by peer”, full process tables, “can not fork process”, mail is dog slow, “file system full”
  Solution(1): Monitor and track mail usage in order to accurately anticipate when mail more resources are needed.

## Slide 53: Electronic Mail
Boom (Mail Bombs)
  Solution (2): Use smap/smapd and
    a: specify maxbytes in netperm-table
    b: handle with scripts and deposit mail into a directory other than /var/spool/smap
    c: handle with “C” code and modify smapd

## Slide 54: Electronic Mail
FQDN (Fully Qualified Domain Name)
  Problem: - Mailhub name specified without fully qualified domain name
  Symptom: - Mail for your domain is not deliverable
  Solution: - When you specify a mailhub name use the fqdn name. Verify that this is what your firewall sees by running sendmail in test mode.

## Slide 55: Electronic Mail
Internal Mailhub does not recognize own domain.
  Problem: Internal mailhub knows own host name but not the domain.
  Symptom: Mail for user@your.domain bounces but mail for user@mailhub.your.domain gets delivered

## Slide 56: Electronic Mail
Internal Mailhub does not recognize own domain (continued):
  Solution: Re-write ruleset 0 in sendmail.cf to re-write mail from user@your.domain to user@mailhub.your.domain.

## Slide 57: Electronic Mail
Trouble Shooting Mail Problems
  Try running Sendmail in test mode
    sendmail -bt
    Test rulesets 3, 0, and 4 minimally.
    You will want to test mail for your domain, outside of your domain, the firewall itself, and any special cases that you have created.
    Also verify that the correct mailer is being used.

## Slide 58: Electronic Mail
Trouble Shooting Mail Problems (continued)
  Telnet to port 25 on the mail server
    You are really looking for the response to the RCPT TO line.
    If you see addressee unknown try VRFY for different spellings.
    If you see host unknown you may have a DNS problem

## Slide 59: Mail and DNS Relationship
No MX record
Eraser ( “You have been erased”)
Child Abuse
Multiple mailhub sharing
Hop, Hop, Hop

## Slide 60: Mail and DNS Relationship
No MX record
  Problem: missing MX record, or MX record is behind a firewall which is blocking DNS requests inbound.
  Symptom: users are able to send mail but are not able to receive mail. The entire domain can not receive mail. Other sites can not respond to your site for mail. Unable to receive internet mail.

## Slide 61: Mail and DNS Relationship
No MX record (continued):
  Solution: Place zone’s MX records on the firewall or the external nameserver. Advertise the firewall as the host accepting mail for the zone.

## Slide 62: Mail and DNS Relationship
Erased
  Problem: This one usually occurs when there is a DNS handoff, and the baton is dropped.
  Symptoms: Noticed when you stop receiving mail and senders mail to your site starts bouncing.
  Solution: You will unfortunately have to start from scratch and register your domain with the InterNIC. A better tactic would be to prevent

## Slide 63: Mail and DNS Relationship
Erased (continued):
  Solution (continued): to have the old nameserver start adding records to mark the new nameserver existence. MX, NS, ...

## Slide 64: Mail and DNS Relationship
Child Abuse
  Problem: Parent domain owns the MX for the child domain (already a delegation problem) then the child domain places a firewall in so the firewall needs to accept mail for the child’s domain.
  Symptom: Can result in mail bouncing back to sender or taking extra hops before arriving at the mailhub

## Slide 65: Mail and DNS Relationship
Child Abuse (continued)
  An example - sub.navy.mil at parent site points to mail.sub.navy.mil and parent won’t budge.
  Solution: Name the firewall mail.sub.navy.mil, have the firewall accept mail for *.sub.navy.mil. Modify sendmail, ruleset 0 so that any mail for user@mail.sub.navy.mil get re-written to go to mailhub.sub.navy.mil for user@sub.navy.mil

## Slide 66: Mail and DNS Relationship
Multiple Mailhub Sharing
  Problem: - Large site has firewalls accepting mail for child domains and has more than one internal mailhub.
  Symptom: - None since this problem is usually identified before the install or at the latest by the installer.

## Slide 67: Mail and DNS Relationship
Multiple Mailhub Sharing
  Solution: - There are 3
    Recommended: Re-write Sendmail ruleset 0
    Ugly aliasing
    Push it off on the internal mailhub

## Slide 68: Mail and DNS Relationship
Hop, Hop, Hop
  Problem: Mail is being bounced. Could be from the internal mailhub not relaying mail out through the firewall. Or could be from the firewall showing MX for internal host and internal host shows MX for the firewall.
  Symptom: Message not delivered too many hops.

## Slide 69: Mail and DNS Relationship
Hop, Hop, Hop (continued)
  Solution: Fix your nameserver so that the firewall accepts mail for your domain. The internal nameserver should not have MX records for your domain pointing to the firewall. Remove the MX record from the internal nameserver.

## Slide 70: Routing
Look packet droppings on the floor :)
No default routes
Static route pointing to the default route
Static route is the default route
Loop-de-loop
ISP routing loops
Multi-homed internal NT hosts

## Slide 71: Routing
Latency and convergence in routing
Load balancing
Load sharing
/etc/route then type what…
netstat -rn
Non routeable IP addresses (RFC 1918)
Using someone else’s IP addresses

## Slide 72: Routing
Look packet droppings on the floor :)
  Problem: Packets are being dropped but not all 100% of them. If packets are not in sequence the connection is dropped and the administrator “sees” a service problem.
  Symptoms: Firewall does not sustain the connection. “Connnection reset by peer”
  Solution: Fix the problem between the hosts. The firewall is working properly.

## Slide 73: Routing
No default routes
  Problem: There is no default route to the firewall by the internal hosts.
  Symptoms: Transparency does not work, “destination unreachable”. Non-transparent access does work.
  Solution: Check the default route on the internal router, or an internal client. Add a default route.

## Slide 74: Routing
No default routes: (continued)
  Solution (continued): Note: If you are running Gauntlet, you can verify by running ipfs in trace mode: ipfs -t and ipfs -t off.

## Slide 75: Routing
No default routes: (continued)
  Another note: Another rarely seen problem with default routes involves having no default route on the firewall. This implies that the site wants to static route to everywhere in the world. The silliness is self-evident, but it does require a mention to the decision makers.

## Slide 76: Routing
Static route pointing to the default route
  Problem: Installed the firewall, specified external router as default route. Able to ping ISP.
  Symptoms: Lots of routing problems. Unable to route on the internet.
  Solution: Not a real one: Static route firewall through external router to the real router with default route.

## Slide 77: Routing
Static route is the default route
  Problem: The default route on the internal host, is confused with a static route.
  Symptoms: Transparency does not work on proxy firewalls. Packets are not forwarded to the firewall.
  Solution: route add default xxx.xxx.xxx.xxx or route add 0.0.0.0 xxx.xxx.xxx.xxx

## Slide 78: Routing
Loop-de-loop
  Problem: You have a routing loop on your end of the network.
  Symptoms: Traffic going nowhere, and slowly at that.
  Solution: Isolate and fix. Some good tools include: ping, netstat -rn, traceroute, show IP routes.

## Slide 79: Routing
ISP routing loops
  Problem: The ISP is suffering from a routing loop problem.
  Symptoms: Traffic is slow. Users are complaining, connections are being reset. Fingers are pointing at the firewall.
  Solution: Unfortunately this one is really out of the site administrator’s hands. A simple traceroute will validate the problem so you can

## Slide 80: Routing
ISP routing loops (continued):
  Solution (continued): address the issue with certainty with your superiors, users and even the ISP. If the ISP knows what they are doing they are probably already aware of the problem. If not, log the problem if this sort of thing happens regularly you may want to consider a new provider and provide your superiors with documentation supporting this decision.

## Slide 81: Routing
Multi-homed internal NT hosts:
  Problem: An internal server was running 2 NIC cards. Default routing was not working, even though specified.
  Symptoms: The default route was to the firewall. DNS forwarding was not working.
  Solution: Added a host route to the NT host for the route to the firewall.

## Slide 82: Routing
Latency and convergence in routing:
  Problem: You found and fixed your routing problem. Now the routes need to propagate
  Symptoms: You did your part to fix the routing problem, but the problem appears to be the same.
  Solution: Either reboot relevant machines in your network, or drink until TTL’s expire.

## Slide 83: Routing
Load balancing:
  Problem: Throughput dictates a need for more than one firewall. Need to balance the load. Load balancing works on packets not sessions.
  Solution: This is another discussion. Some vendors like to recommend “DNS Round Robining” but that is load sharing. Possible traffic direction to firewall by port performed by the router.

## Slide 84: Routing
Load sharing:
  Problem: High throughput, more than one firewall. Packets are not balanced, one firewall could have a light load while the other firewall is being brought to its knees.
  Solution: DNS Round Robining, don’t confuse it with load balancing.

## Slide 85: Routing
/etc/route then type what?
  Problem: Lack of familiarity with routing commands
  Symptoms: General confusion regarding taking control of your routes.

## Slide 86: Routing
/etc/route then type what? (continued):
  Solution: Here are some basics:
    route add default xxx.xxx.xxx.xxx
    route add 0.0.0.0 xxx.xxx.xxx.xxx
    route add -net xxx.xxx.xxx yyy.yyy.yyy.yyy {-netmask}
    route add host xxx.xxx.xxx.xxx yyy.yyy.yyy.yyy
    route flush

## Slide 87: Routing
/etc/route then what? (continued):
  Solution (continued):
    route delete default
    route delete -net xxx.xxx.xxx yyy.yyy.yyy.yyy
    route delete -host xxx.xxx.xxx.xxx yyy.yyy.yyy.yyy
    route delete 0.0.0.0 xxx.xxx.xxx.xxx
  Note: Know the difference between host routes and subnet routes. Sometimes a netmask option goes a long way.

## Slide 88: Routing
netstat -rn
  Problem: Need to know routing info
  Symptoms: What are my routes
  Solution: netstat -rn, verify your routes.
show IP routes
  Problem: Need to know routing info
  Symptoms: What are my routes
  Solution: show IP routes (if your firewall is a router)

## Slide 89: Routing
Non routeable IP addresses (RFC 1918)
  Problem: No problem using them, but be sure to keep them on the internal network, or behind a NAT.
  Symptoms: Internet users unable to route to these hosts.
  Solution: Hosts using RFC 1918 must be behind a NAT. Routing to those hosts must be through the firewall or NAT host.

## Slide 90: Routing
Using someone else’s IP addresses:
  Problem: Decided to use the firewall to perform NAT and “stole” someone’s IP address.
  Symptoms: Can not go to the real IP address.
  Solution: Use IP addresses specified in RFC 1918

## Slide 91: Subnetting
0 and 1 usage and the old 128 mask
.255 is a illegal address
VLSM with a Firewall OS that does not!
Network topology <> network numbering

## Slide 92: Subnetting
0 and 1 Usage and the old 128 netmask
  Using the 0 net (references the network by 0 therefore, implies that you plan on using the entire network).
  Using the all 1 network makes use of the 255 broadcast. Again, implies that you plan on using the entire network.
  The 128 netmask would then be illegal!!! (But it still happens!)

## Slide 93: Subnetting
0 and 1 Usage and the old 128 netmask (continued)
  Problem - Using non standard subnets.
  Symptom - Static routes to network show up in your routing table as host routes.
  Solution - Do it right!

## Slide 94: Subnetting
The next few slides show some commonly used subnetting examples: The italicized rows indicate the unusable nets.

## Slide 95: Subnetting
Network
Broadcast
Netmask
Useable Hosts
0
192.1.92.63
255.255.255.192
1-62
64
128
192
192.1.92.127
255.255.255.192
65-126
192.1.92.191
255.255.255.192
129-190
192.1.92.255
255.255.255.192
192-254

## Slide 96: Subnetting
Network
Broadcast
Netmask
Useable Hosts
0
32
64
96
128
160
192
224
192.1.92.31
192.1.92.63
192.1.92.95
192.1.92.127
192.1.92.159
192.1.92.191
192.1.92.223
192.1.92.255
255.255.255.224
255.255.255.224
255.255.255.224
255.255.255.224
255.255.255.224
255.255.255.224
255.255.255.224
255.255.255.224
1-30
33-62
65-94
97-126
129-158
161-190
193-223
224-254

## Slide 97: Subnetting
.255 as a Legal Address
  Problem - 255 is not a legal host address!
  Solution - Don’t use 255 as an address.

## Slide 98: Subnetting
VLSM with a Firewall OS which does not!
  Problem: Network is subnetted using a variable length subnet mask (VLSM) and firewall OS does not support VLSM
  Symptom: Network routes show up as host routes in routing tables. Things generally don’t work.

## Slide 99: Subnetting
VLSM with a Firewall OS which does not! (continued):
  Solution: Keep the 2 networks on the firewalls two interfaces static. Place a router behind the firewall and use VLSM on the segment not directly connected to the firewall. Planning helps a lot here.

## Slide 100: Subnetting
Network Topology <> network numbering
  Problem: Documented network topology indicates a different network numbering scheme.
  Symptoms: If using host based or network based security is utilized, authorization administration becomes a nightmare, since network documentation does not match what firewall knows.

## Slide 101: Subnetting
Network Topology <> network numbering
  Solutions: Update network documentation and clearly identify hosts and networks. Administration of host based and network based security is lessened. If network numbering is changed, all documentation related to network topology should be updated(CTFM). Revision control processes. Audit trail, and system configuration should be up to date.

## Slide 102: Virtual Private Networks
What firewall vendors don’t tell you about VPNs
Failover VPN (nonexistent)
Poor planning of VPN network
  Reverse Darwinism
  Saving address space from RFC 1918
Know you pairs limits

## Slide 103: VPNs
What firewall vendors don’t tell you about VPNs
  Utilize network level encryption:
    This is contrary to application and user level security; therefore, application gateways have broken their consistency model
    Cisco and Checkpoint at least have consistent models

## Slide 104: VPNs
What firewall vendors won’t tell you about VPNs
  Some proxy solutions claim to have a hand-off to the application layer, but they don’t release the source code.
  Transitive trust issues abound!
  IPSEC compliance was added to allow various firewalls to interoperate, but does not address different security architectures.

## Slide 105: VPNs
Failover VPN (nonexistent)
  Problem: A VPN realm with a subset of a VPN network fails and cannot dynamically re-establish its connection with the other realms.
  Symptom: Firewall vendor stated it clearly in its sales material, that this feature does work
  Solution: Seek out other network redundancy solutions (i.e. BGP with two different ISPs, for every VPN realm or 56k/ISDN solutions)

## Slide 106: VPNs
Poor planning of VPN network
  Reverse Darwinism
  Saving address space from RFC 1918

## Slide 107: VPNs
Poor planning
  Reverse Darwinism
    Problem: Multiple security policies across a VPN with complete trust. The weakest security policy wins.
    Symptom: Security breaches, may even go undetected.
    Solution: This unfortunately is a serious problem which requires both training or decision makers along with giving administrators the ability to

## Slide 108: VPNs
Poor planning
  Reverse Darwinism
    Solution (continued): enforce the policy. VPNs can be a viable solution to some problems, but they should be well designed. If you can not enforce the your security policy with the other “trusted” network then you should not be setting up a VPN with that site and your internal network! Note: You can set up a VPN on a new interface.

## Slide 109: VPNs
Poor Planning
  Saving address space from RFC 1918
    Problem: Both sites decided to do the politically correct thing and use the non routeable addresses in RFC 1918, unfortunately they both chose the same network. :(
    Symptoms: Can not route to the destination network
    Solution: Good upfront planning, or NAT to the rescue.

## Slide 110: VPNs
Know your pairs limits
  Gauntlet: 99
  Eagle: 15 (known)
  Firewall-1: 30

## Slide 111: Authentication
OK, show me your ID! (We don’t need no stinkin’ badges :)
Sharing authentication servers
FWTK and Gauntlet netperm-table mods
ACE Server and DNS Relationship (yep, they have one too!)
Reuseable passwords
Asking permission to surf

## Slide 112: Authentication
Password sharing with the secretary
Trusting your staff
Single Sign-on

## Slide 113: Authentication
OK, show me your ID
  Authentication - the process in which users are identified, validated and granted access.

## Slide 114: Authentication
Sharing Authentication Servers
  Problem - More than one firewall in parallel wants to share one authentication server, but something is not set up properly ;)
  Symptoms - Authentication only works with one firewall but not the others.
  Solution - Make sure the firewalls are communicating on the correct ports, and referencing the same database location.

## Slide 115: Authentication
FWTK and Gauntlet Netperm-table mods
  Server
    When sharing the authserver the client IP address must be specified on the server in the netperm-table.
  Client
    Remember to build the authsrv first (if not already done)
    Specify the server IP address in the netperm-table

## Slide 116: Authentication
ACE Server and DNS
  Problem - ACE Server is resolving off of a different nameserver than the one that the firewall is using. Record for the firewall is either missing or incorrect.
  Symptom - ACE Server returns an error usually indicating that the host is invalid.

## Slide 117: Authentication
ACE Server and DNS
  Solution - Either have the ACE Server resolve off of the same nameserver as the firewall or modify the nameserver that the ACE Server is using.
  BTW - Don’t forget to RTFM and move over /var/ace/sdconf.rec

## Slide 118: Authentication
Reuseable Passwords (this one seems so obvious why are we even discussing it?)
  Problem: Using reusable passwords to authenticate services.
  Symptoms: Unauthorized access, odd behavior for particular users.
  Solutions: DO NOT USE REUSEABLE PASSWORDS!!! Use a network monitoring tool.

## Slide 119: Authentication
Asking permission to surf (a type of social engineering)
  Problem: Authentication for outbound web access.
  Symptom: None, except not the best security model.
  Solution: Prevention is the best solution. Logs of user web access may not be very reliable.

## Slide 120: Authentication
Password sharing with the secretary (Security is for everyone)
  Problem: The “Big” guy does not have time to read his email, therefore, an administrative assistant not only is given his email password but also system password, to check other items..
  Symptoms: “Not getting flowers on Secretary’s Day” can cause a lot of problems :)

## Slide 121: Authentication
Password sharing with the secretary (Security is for everyone) (continued):
  Solution: Allowing someone else the ability to log on as you is a very poor decision and not advised at all. If the “Big” guy is to busy to read email, an AUTO-RESPONDER or /usr/ucb/vacation mail is a better and a wiser solution.

## Slide 122: Authentication
Trusting your staff (multiply your security problems by the number of staff)
Segment staff access, need to know

## Slide 123: Authentication
Secure Single Sign-On
  Secure single sign on, promise LDAP compliance
  Lots of vendors want to sell you their single sign on products.

## Slide 124: Authentication
Secure Single Sign On (continued)
  Make sure that if they say it is using TCP calls that it really does.
    RPC != TCP
    How can you have authentication with 100% assurance without a socket?
  Presently most firewalls do not support single sign-on products. But they will eventually have to.

## Slide 125: Authentication
LDAP - Lightweight Directory Access Protocol
  Lookup service to find users throughout the internet.
  Port 337/TCP, commonly used for directory server look up (I.e.. ldap.bigfoot.com, ldap.four11.com, ldap.schoolmates.com)
  Software used to invoke LDAP varies from vendor to vendor. For example, Micro$oft :(

## Slide 126: Trust Relationship
Multiple levels of trust
Trust is such a transitive thing

## Slide 127: Trust Relationship
Multiple levels of trust
  Problem: This is usually an architecture problem. Multiple trust domains on a single wire. Administrator got confused when setting up the various entities and their rulesets.
  Symptoms: Some services work for some users but not consistently.
  Solutions: KISS, Good policies.

## Slide 128: Trust Relationship
Trust is such a transitive thing:
  Problem: Host based trust or network based trust results in you absorbing someone else’s security policy.
  Symptoms: None until too late :(

## Slide 129: Trust Relationship
Trust is such transitive thing: (continued)
  Solutions: A well defined security matrix that details the following: risk analysis, network use policy, user authentication and authorization. ( i. e. allowing/restricting a host by destination and/or service). An examination of the software being used for security. Finally, good coding and standardization of documentation practices should be adhered to.

## Slide 130: Cabling
How long is your cable?
Cabling different but connector is same
Connector is different but cable is same
Connector is different and so is cable
Terminate who? ;)
Crossover vs hub (I need a what?)
LAN SPEEDER problems

## Slide 131: Cabling
How long is your cable?
  Problem: 10 Base T requires minimum cable length
  Symptom: Card is alive but can not ping
  Solution: Minimum 6ft length, can be longer

## Slide 132: Cabling
Cabling different but connector is same
  Problem: Different cables into the same connector (such as token ring and ethernet)
  Symptom: Everything is connected but nothing talks
  Solution: Match card and cable based on network topology. Color coat your cables. Label your network

## Slide 133: Cabling
Connector is different but cable is the same:
  Problem: One end of the cable is a different type of connector than the other end. Or end connector is not wired correctly.
  Symptom: Blinky on one end, but not on the other, no connectivity between devices
  Solution: Verify that all connectors are of the same type and made the same way

## Slide 134: Cabling
Connector is different and so is cable:
  Problem: Cable and connector not compatible.
  Symptom: Nothing connects.
  Solution: Match hardware and cabling with network topology.

## Slide 135: Cabling
Terminate, who ;)
  All connectors if needed
  Problem: Unterminated connections, dead connections.
  Symptom: No connectivity
  Solution: If using thin net use “t’s” and terminators, if using 10 base T use hubs or crossover cables.

## Slide 136: Cabling
Crossover vs hub
  Problem: Tried to connect the router directly to the firewall.
  Symptom: Lights off! Nothing works.
  Solution: Put cables into the hub or use a crossover cable. Cross pairs n &n and m&m

## Slide 137: Cabling
LAN Speeder problems:
  Problem: Internal network rated higher (faster) than the firewall
  Symptom: Dog slow throughput on the firewall
  Solution: Ensure size and capability of firewall is rated to sustain internal network for specific needs.
    1 M RAM /10 users

## Slide 138: Filtering Rules
Odd and Even packet flow
Rule set blocks all traffic including firewall
Sorting rule sets alphabetically (d before p)
Firewall rules written, but NAT forgotten

## Slide 139: Filtering Rules
Odd and even packet flow
  Design of network was divided up on even and odd based host addressing space. Filter rule set implemented based on this.
    permit 10.0.0.1 est tcp 25
    deny 10.0.0.2
  Problem: Monster access list causes throughput problems

## Slide 140: Filtering Rules
Odd and even packet flow (continued):
  Symptom: Firewall is slow because it has to parse through the entire access list.
  Solution: If you are designing access control lists plan them out on paper, and manually walk through all the rules. Rules can be either common English sentences or coded based on the particular firewall language. Example: “If not explicitly permitted, then it is denied implicitly.”

## Slide 141: Filtering Rules
Rule set blocks all traffic including firewall
  Problem: Bad ruleset implemented on firewall or misconfigured rule set
  Symptom: No traffic is being allowed through firewall.
  Solution: Remove the problem rule without changing the security policy. General rules should be the last one in the list.

## Slide 142: Filtering Rules
Sorting rule sets alphabetically (d before p)
  Problem: Deny rules before permit rules.
  Symptoms: Nothing works as planned.
  Solution: Really this is a mixed bag. There are some things that you want to deny first (source routed packets, icmp redirects, “ip spoofing”…). General rules go on the end. Deny all for all services should be the last rule.

## Slide 143: Filtering Rules
Firewall rules written, NAT forgotten (1)
  Problem: Wrote a great access list but forgot to do NAT.
  Symptom: Outsiders are able to gain info on internal network addresses.
  Solution: Turn on the network address translation, shorten your perimeter. Don’t want the outside world to be able to map out your internal network.

## Slide 144: Filtering Rules
Firewall rules written, NAT forgotten (2)
  Problem: Wrote a great access list but forgot to consider NAT.
  Symptom: Outside server denies access.
  Solution: Outside server needs to allow access from the firewall’s translated address (external interface on proxy servers).

## Slide 145: Filtering Rules
Firewall rules written, NAT forgotten (3)
  Problem: Wrote access control lists but forgot about the trusted network.
  Symptom: Internal users can not get out.
  Solution: When writing access lists remember to write for both trusted and untrusted (along with any other policy).

## Slide 146: TCP Wrapper
What does it do?
How might it improve my security life?
Some cases where it has saved some folks.
Tastes like chicken

## Slide 147: TCP Wrappers
TCP Wrapper - (NetACL)
  For FWTK and Gauntlet types
  Netacls provide you the ability to run more than one service on the same port.
  Can be used to split processing by host addresses (sort of like a traffic cop, so can ipfilterd but that is later)
  Addresses some of the shortcomings of having proxy servers.

## Slide 148: TCP Wrapper
TCP Wrapper
  Two files need to be modified in order to get this work.
    The file which starts off the proxies such as rc.local or inetd.conf
    Netperm-table needs to be modified to indicate which host(s) get which service on the port to the final destinations

## Slide 149: TCP Wrapper
How might it improve my security life
  Allows you the ability to gather extra logging on services.
  Allows you the ability to specify specific services for specific host pairs

## Slide 150: TCP Wrapper
Some cases where it has saved some folks:
  Problem: FTP was running on port 21 (and 20)A home grown application had to connect to an internal host on port 21 in order to perform an update. The firewall had to support both services.

## Slide 151: TCP Wrapper
Some cases where it has saved folks:
  Solution: By “splitting the netacls” we were able to specify that traffic from the host with the home grown to use the generic proxy. All other hosts used the FTP proxy.
  Solution: Run a packet filtering solution if it fits your security policy.

## Slide 152: TCP Wrapper
Tastes like chicken
  Grilled and salted anything tastes like chicken.

## Slide 153: System Logging
Turning off the logging
Missing loghost record
Not enough disk space
Failure to pay proper attention to the logs
Turning off annoying alerts in the logs
Seeing an alert and responding improperly

## Slide 154: System Logging
Back doors into network tripping off “IP Spoofing” Alerts.
Overreacting to alerts
Why do I need to check the logs, they are too big?

## Slide 155: System Logging
System logs when properly maintained are a vital piece of any firewall system. They provide the recording of your firewall’s activities. In the event of a security breach the system logs are often times used to reconstruct the events that took place. Therefore, do not ever do anything which can comprise the integrity of your system logs.

## Slide 156: System Logging
Turning off logging
  Problem: Someone determined that logging was using too many CPU cycles, and way too much disk space.
  Symptoms: No logging info!
  Solutions: Try logging to another host that can handle the load. Modify /etc/syslog.conf to specify the host. Use IP addresses instead of host names, make sure logging host is in internal network.

## Slide 157: System Logging
Missing loghost record
  Problem: System logging is not working because the loghost is not defined (SUN OS).
  Symptoms: No logging, checking syslog.conf reveals all is well. Restarting the syslogd does not fix the problem.
  Solution: Add the following DNS record if you are logging on the firewall box: loghost IN A 127.0.0.1

## Slide 158: System Logging
Not enough disk space
  Problem: Many firewalls continue to pass traffics as per their design when the logs are full and they are unable to log data.
  Symptoms: Logs are not growing. Missing entries. No logging is taking place.

## Slide 159: System Logging
Not enough disk space (continued):
  Solution: Cron to the rescue. Periodically check your disk space on the partition which is logging. If you have a short memory write a script file to do it for you and make it a cron job.

## Slide 160: System Logging
Failure to pay proper attention to the logs:
  Problem: There is no problem visible, administrator sees nothing.
  Symptoms: Fat dumb and happy administrators.
  Solution: Read your logs! Security requires due diligence. Understand your logs. If you don’t understand the logs get training, ask the vendor or hire consultants. Get some good reduction tools.

## Slide 161: System Logging
Turning off annoying alerts in the logs.
  Problem: Repeated log entries usually indicating a security alert of some sort.
  Symptoms: System logs get swamped with alerts so the fwadmin turns off the alerting mechanism in the logs.
  Solution: Fix the source of the problem. If you are unable to fix the source, then turn off the alerts on your firewall log located on the

## Slide 162: System Logging
Turning off annoying alerts (continued):
  Solution (continued): firewall but keep the alerts on for shadow logging.

## Slide 163: System Logging
Seeing an alert and reacting improperly
  Problem: Once again the security alerts are annoying.
  Symptom: The fwadmin is being overwhelmed with security alerts, and knows to not shut off the logs. (Was awake for the last slide) Therefore, opens a hole in the firewall to make things work.

## Slide 164: System Logging
Seeing an alert and reacting improperly (continued):
  Solution: Fix the problem. Barring that, redesign (or rearchitect) to fit both the security policy and the internet use policy.

## Slide 165: System Logging
Back doors into network tripping off “IP Spoofing” Alerts
  Problem: Security alert indicates traffic landed on the wrong interface.
  Symptoms: Operator thinks they are witnessing an “IP spoofing” attack.
  Solution: Close the back doors into the network and see if alerts go away (they usually do).

## Slide 166: System Logging
Over Reacting to Alerts
  Problem: Security alerts of any sort, along with no procedures for handling alerts (read no security policy)
  Symptoms: Inconsistent responses ranging from ignoring alerts to calling in 3 letter agencies.

## Slide 167: System Logging
Over reacting to Alerts (continued):
  Solution: Read the alerts. Check the of source and destination IP addresses along with the port numbers. Sometimes a little detective work is in order. Traceroute to the source, nslookup or dig on the source IP address. Check /etc/services to find out the service. It may be something stupid (like netbios). Follow procedures specified in policy.

## Slide 168: System Logging
Overreacting to alerts (continued)
  Solution (continued): If you are legitimately being attacked and have a security policy then, follow your sites procedures and make sure your logging is working. If you are legitimately being attacked and have no security policy them, you are in a bad spot, but that is no reason to hand over the keys to the kingdom. You can try letting the source know what is going on and request an end to it. Keep logging, verify the security of your own site so that they can not use your site.

## Slide 169: System Logging
1,2,3, REDLIGHT .. 1,2,3, GREENLIGHT
  Problem: Rule set built but coded incorrectly. Example: permit * est tcp 79 /usr/ucb/finger -nolog
  Symptoms: Events that should have raised some eyebrows, flags or alerts gets ignored by the system or gets dropped.
  Solutions: Re-evaluate rule sets and event logging to ensure proper logging and stubs

## Slide 170: Backups
Remote Backups
Update scripts
Didn’t need that file
Backup, nothing ever happens here
Someone has to load tapes
Log refresh
Verify backups work

## Slide 171: Backups
Remote Backups
  Problem: Don’t have back up facilities
  Symptoms: Don’t do backups. Or do backups over the internet.
  Solution: If doing remote backups do them locally with hosts on your internal network and verify that they work. Backups done over a public network are generally unencrypted.

## Slide 172: Backups
Backup, nothing happens here
  Problem: Nothing exciting happens here. Administrator does not see anything relevant happening. If the firewall was purchased, even if it sits in a corner unused, it has value to the company, therefore, it should be backed up.
  Solution: Do your backups, they are good for your health.

## Slide 173: Backups
Update scripts:
  Problem: Person had a customized file system layout with three partitions. Firewall assumed two partitions. Script was updated on initial install.
  Symptom: Error spewing on dump script
  Solution: Keep track of customized files, save separately, then merge into updates.

## Slide 174: Backups
Someone has to load tapes
  Problem: Performed the backup, never verified that it worked.
  Symptom: Can not restore off of current backup.
  Solution: None really, verify the backup tapes work.

## Slide 175: Backups
Log refresh
  Problem: Backups are performed but not in sync with log refreshing capabilities.
  Symptoms: Some logs are never saved, which makes for a difficult time in trying to recreate events.
  Solutions: If you refresh your logs on an interval of 1 week do your backups weekly!

## Slide 176: Indiscriminate use of Generic Proxies
Home growns, we just code around it
Host-based authentication

## Slide 177: Indiscriminate Use of Generic Proxies
Home growns, we just code around it
  Problems: Home grown code uses TCP sockets so can pass through a generic proxy.
  Symptoms: None, but there exists a security problem
  Solutions: Code should be reviewed to ensure that such problems as buffer overruns, error conditions, and user privs are dealt with in a secure manner, to name but a few items here!

## Slide 178: Indiscriminate Use of Generic Proxies
Home grown, we just code around it (continued):
  Note: A generic proxy is not much different than a packet filter, you may be opening up your site to data driven attacks!

## Slide 179: Indiscriminate Use of Generic Proxies
Host based authentication
  Problem: Use of a generic proxy which utilizes host based authentication.
  Symptoms: You may never see them
  Solutions: Examine the need to use the service and when at all possible place on a service network or a DMZ. Generic proxies can be compromised through data driven attacks and unauthorized access.

## Slide 180: Operating Systems Goodies
System Leftovers (HP field account, SGI - guest, SUN - NIS, Livingston - !root and no password)
Supported by kernel but not application
Support by application but not kernel
Midnight Specials
Vulnerabilities

## Slide 181: Operating System Goodies
rc.local and inetd.conf to start up together
Unable to bind

## Slide 182: Operating System Goodies
Supported by kernel but not in application:
  Problem: This usually happens with hardware like NICs and SCSI cards.
  Symptom: Device not seen on bootup
  Solution(1): Find the device in the kernel configurable, compile; make; make depend; mv… (as per OS instructions)
  Solution (2): Take a class on writing device drivers, you’re going to need it.

## Slide 183: Operating System Goodies
Supported by application but not in the kernel:
  Problem: Device is supported by application but not kernel.
  Symptom: Aborted build, partial install.
  Solution: Use recommended hardware and operating system (version too!)

## Slide 184: Operating System Goodies
Device Drivers
  Problem: The particular case that comes to mind is one in which the same host was used to evaluate various firewalls. One firewall product removed some of the system device drivers during it’s install process. The next firewall needed to use the missing device drivers.

## Slide 185: Operating System Goodies
Device Drivers (continued):
  Symptom: Some things work as advertised, others do not. In this particular case transparency did not work.
  Solution: When using the same host to evaluate firewalls, you should re-install the OS first before installing the new firewall

## Slide 186: Operating System Goodies
Back Doors
  Problem: Vendors leaving backdoors into the OS to assist in support.
  Symptom: None really, but this is a rather large security problem.
  Solution: Most firewall install scripts remove vendor backdoors into the network, but you need to verify this is indeed the case.

## Slide 187: Operating System Goodies
rc.local and inetd.conf to start up together
  Problem: Two or more services start on the same port.
  Symptoms: “Unable to bind to port n, already in use.
  Solution: One service per/port, if you need to run more than one through use a TCP wrapper on proxy based firewalls.

## Slide 188: Operating System Goodies
Unable to bind …
  Problem: OS inetd only supports so many connections.
  Symptoms: Can not start any more connections, inetd looping.
  Solution: Try running proxies in daemon mode instead of out of 1 daemon.

## Slide 189: Operating System Goodies
What is my operating system trying to tell me:
  ps - Process table tells you what is running. Should be those processes that you specify and nothing else. “Turn off everything then turn on required services one at a time.”
  tops - Who’s hogging the CPU!
  df - File system usage

## Slide 190: Fine Print from the Vendor
How big??
Authentication with licensing
WARNING, Will Robinson, WARNING
Minimal requirement is not always the best recommendation

## Slide 191: Internal Network Protocol Suite
IPX
Microsoft
Banyan
etc...

## Slide 192: Internal Network Protocol Suite
IPX
  Problem: Older versions of IPX claim to be IP compliant but are not.
  Symptom: Services do not work, commonly DNS fails (this is usually a tip-off).
  Solution: Run the most recent version; otherwise, install vendor patches.

## Slide 193: Internal Network Protocol Suite
Microsoft
  Problem: Where to begin on this one! Most common; netbios causing alert problems.
  Symptom: Security alerts ports 137, 138 and 139.

## Slide 194: Internal Network Protocol Suite
Microsoft
  Solution: Avoid using M$ products whenever possible. ;) Seriously, be aware of problems with Microsoft products, be aware of how they are designed and working, monitor closely for security breaches.

## Slide 195: Internal Network Protocol Suite
Banyan Vines
  Problem: Street talk
  Symptoms: Other Banyan servers find each other via broadcasts, “street talk”. This is not a good thing to pass through firewalls.
  Solutions:
    Change architecture
    Packet filtering with NAT
    VPNs

## Slide 196: Back Door
Couldn’t afford it
Vendor pick-up
Those Sales people promise you the world don’t they
What is behind DOOR #3
Remote Power Management and Emergency Intervention
Installers leaving backdoors!

## Slide 197: Back Door
Installers leaving back doors (more common than you think!!!)
  Problem: Installers leave a back door onto the firewall so that they can get in to administer it in the event of trouble.
  Symptoms: None, unfortunately.

## Slide 198: Back Door
Installers leaving back doors (more common than you think!!!)
  Solution: COPS, Tripwire, inspection question anything suspicious. Some companies mandate installers leave in back doors, don’t let them do it on your network!!!

## Slide 199: Security Administration Procedures
Root access
  Problem: Security administration policy states the following: “The root password must be changed on an unannounced basis every 40 days. “
    The reason explaining this type of policy is due to the password of the root account must not be compromised as this would allow an unauthorized user unlimited access to the system.

## Slide 200: Security Administration Procedures
Root access
  Symptom: The root user is the most powerful account in the UNIX environment.
  Solution: Policy sounds great, but what does it really state. Root account should be changed every 40 days, and explains what root does.

## Slide 201: System Administration Procedures
(Solution cont.:) The real solution is design a policy that fits within your environment and state clearly why passwords should be changed on a timely basis, especially root. The statements regarding at the potential dangers of certain privileged accounts should be listed, but also in your infinite wisdom of system administration, you can limit what applications are potentially dangerous if run as root and modify the applications to run under lesser privileged accounts.

## Slide 202: System Administration Procedures
Root access
  Problem: Policy states : “All systems must disable direct root login, except for the console.”
    States the reason why: “This is a security concern for two reasons; first, it denies any user on the network the opportunity to guess the root password by performing multiple login attempts from the local workstation.

## Slide 203: System Administration Procedures
  (States reason why cont:) Second, the ability to login directly as root (without first logging into a non-privileged ID) limits accountability for activities performed by root.
  Solution: There are many solutions around this type of policy to prevent wordy type things to appear in policy. The use of authentication devices on top of privileged account access will eliminate paper in your policy.

## Slide 204: System Administration Procedures
Emergency Passwords
  Problem: Data security must have passwords available for emergencies.
  Symptom or policy stating why: Often the root password is widely disseminated in the event of an "emergency.”

## Slide 205: System Administration Procedures
  A Solution: Passwords will be kept in a secure storage device to which unauthorized access can be easily detected. A locked box containing a sealed envelope for each password, for example.
    A Twist : The above issue can be avoided by creating generic operator accounts with restricted shells/menus for level 1 diagnostics (I.e. ping, traceroute, nslookup )and refrain from enveloping hogging.. and losing the key syndrome :)

## Slide 206: Network and Security Policy
Network and Security Policies are important since a commercial firewall product is only a small piece of the overall design of a firewall system and internet solution.
  A firewall is an access control device, used to implement a security policy.

## Slide 207: Network and Security Policy
Many policies were written a long time ago prior to the so-called “Internet Age”.
Network policies should be living documents as your network grows.

## Slide 208: Network and Security Policy
Policy second?
  Problem: Policies are done last after a firewall has been installed.
  Symptom: Network policy doesn’t document the risk of having a firewall.
  Solution: Evaluate risks of being on the internet and how the company within will use the firewall in the company.

## Slide 209: System Architecture
Various architectures will have different effects on your firewall. For example: If you are packet filtering in parallel to proxying then you may have problems with the proxy firewall “ip spoofing” alerts.

## Slide 210: System Architecture
Single Homed
“Screened Subnet”
Dual Homed
“Belt and Suspenders”
Tri Homed
High Speed
  Load balancing vs Load sharing

## Slide 211: System Architecture
VPNs
‘Sample’ of all
Remote Access
  With or without restrictions
Future

## Slide 212: System Architectures
Single Homed
  Pros:
    Easy migration
  Cons:
    Less secure
  Considerations:
    Does not require running a nameserver on the firewall.
    Does not require a MX record to be advertised on firewall, but it should be.
Internet

## Slide 213: System Architecture
Screened Subnet
  Pros:
    Works well in non-IP environments
  Cons:
    Perimeter is wider
  Considerations:
    Installation is not disruptive
    Gateways may have problem w/ smoke alarms
Internet

## Slide 214: System Architecture
Dual Homed
  Pros:
    Very Secure
  Cons:
    Throughput concerns with large organizations
    Requires users to know all traffic
  Considerations:
    DNS and Mail requires planning
Router
Firewall
web
host
host
Internet

## Slide 215: System Architecture
“Belt and Suspenders”
  Pros:
    Appears more secure
  Cons:
    Troubleshooting can be difficult
  Considerations:
    External router could be stateful inspection firewall w/ NAT
    DNS, Mail, FTP
Router
Firewall
web
host
host
Internet
Router
Router

## Slide 216: System Architectures
Tri Homed
  Pros:
    Provides more security on web (or DMZ) transactions
  Cons:
    Throughput may be an issue
  Considerations:
    Need to know and understand differing policies
Router
Firewall
web
host
host
Internet

## Slide 217: System Architectures
High Speed
  Pros:
    Handles higher volumes of traffic
  Cons:
    Reconcilation of configs
  Considerations:
    If load sharing do not run a caching ns.
    Load balancing vs load sharing
Router
Firewall
web
host
host
Internet
Firewall
Firewall

## Slide 218: System Architectures
VPNs
  Pros:
    Encryption makes the internet a private net
  Cons:
    Tunnels around the firewall, traffic is not audited
  Considerations:
    Watch out for RFC 1918
    Transitive trust
    IPSEC merges models
Host A
Host B
Firewall A
Firewall Z
Host Z
Host Y
Internet

## Slide 219: System Architectures
‘Sample of All’
  Pros:
    Addresses short comings of VPNs
  Cons:
    Requires planning and understanding of traffic flow
  Considerations:
    Implementation may be tricky
F/Wall
F/Wall
LAN
LAN
VPN
IDD
IDD
IDD

## Slide 220: System Architectures
Remote Access
  Pros:
    Privacy
  Cons:
    Requires client software
  Considerations:
    Some remote access solutions use tunneling therefore can not audit and use host based authentication.
Router
Firewall
web
host
host
Internet
Client

## Slide 221: System Architectures
Future
  Pros:
    Side steps political issues.
  Cons:
    Distributed management
  Considerations:
    Most firewalls are not designed to act as a defense for a large corporation
F/Wall
IDD
F/Wall
IDD
F/Wall
IDD
LAN
LAN
LAN

## Slide 222: Internet Security Reviews
Problem: Installation/implementation of firewall is complete but how do you know if properly installed.
Symptom: Testing for vulnerabilities yields results which indicate site is vulnerable
Solution: There are some tools commercially and freely available to help.

## Slide 223: Internet Security Reviews
Solution(continued):
  ISS - Internet Security Scanner (SafeSuite). is an automated network analysis tool that scans a predetermined range of IP addresses and performs approximately 155 penetration tests aimed at exploiting known vulnerabilities in TCP/IP based network services.

## Slide 224: Internet Security Reviews
Solution (continued):
  Some of the tests performed by ISS:
    sendmail/SMTP security weaknesses
    susceptibility to brute force attacks
    insecure TFTP and FTP setups
    NTFS vulnerabilities,
    NETBIOS SMB easy password vulnerability
    Root.. vulnerability, CD.. vulnerability,
    rpc service vulnerabilities,
    Various NETBIOS vulnerabilities, and other IP based attacks

## Slide 225: Internet Security Reviews
Solution (continued): Scanning tools
  Ballista - an automated network analysis tool. Ballista scans a predetermined range of IP addresses and performs over 200 penetration tests aimed at exploiting known vulnerabilities in TCP/IP based network services. Ballista also performs extremely comprehensive and esoteric network based attacks including:

## Slide 226: Internet Security Reviews
  Ballista checks:
    Network and protocol spoofing checks,
    Source Routed rlogin, rsh and telnet checks,
    RIP and ARP spoofing checks, IP Forwarding check,
    DNS Resource record check, DNS reverse lookup,
    DNS Cache corruption check,
    DNS out of sequence check,
    Additional DNS cached information answer check,
    DNS denial of service check,
    DNS Cached answers with a binary data check

## Slide 227: Internet Security Review
  Ballista checks (continued):
    IP fragmentation (tiny) check,
    IP fragmentation (overlay) check,
    IP forwarding check,
    Internal based addresses check,
    ICMP netmask request check,
    ICMP timestamp check,
    ICMP check68,
    MBONE packet encapsulation check,

## Slide 228: Internet Security Review
  Ballista checks
    APPLETALK IP, and IPX encapsulation checks,
    Reserved bit check,
    Source porting via TCP and UDP checks,
    Odd protocol check,
    TCP and UDP ports filter checks,
    Exhaustive TCP and UDP ports checks,
    Zero length TCP and IP options filter checks,
    Oversized packet check, and,
    Post-EOL TCP and IP options checks.

## Slide 229: Internet Security Review
Scanning Tools (cont):
  SATAN - Security Administrator’s Tool for Analyzing Networks for UNIX by Dan Farmer and Wietse Venema
  Homegrowns - combination of scripts that your own system administrators have put together to test particular to their needs .

## Slide 230: Internet Security Reviews
Each of the tools that have been described in slides presented earlier has its advantages and disadvantages. Each tool can give you a different picture about your firewall. Some of the tools run together can give you an even better picture. Vulnerabilities are discovered on a hourly basis depending who you talk to. Picking the right tools is for you to decide. Configuring them to work correctly can be another tutorial in and of itself. :)

## Slide 231: Internet Security Review
Problem: Analysis of data from commercially and freely available tools are easy to analyze
Symptom: Firewall passed some tests but vulnerabilities were found
Solution: Risk analysis and resources play a key in vulnerability assessment and assigning resources to address the problem and executing corrective action.

## Slide 232: Internet Security Reviews
Firewall installed and user wants assurance/validation:
  Problem: Similar to the previous problem. A user has a firewall installed. Now the user wants some verification that the firewall is secure.
  Solution: In addition to scanning software, attestation of the firewall code is required. The code should be examined for good coding

## Slide 233: Internet Security Reviews
Firewall installed, user wants assurance/validation (continued):
  Solution (continued): practices: minimally coded, clean logic paths, error checking, overrun checks, race conditions, ect. This requires availability of source code. Also remember your intrusion detection devices.

## Slide 234: Internet Security Reviews
User does not understand ramifications of selected firewall architecture:
  Problem: Firewall properly installed, access lists set exactly as user specified.
  Symptom: Network scan reveals vulnerabilities.
    Example: Purchased a packet inspection firewall and build access list to allow mail to internal mailhub. Internal mailhub is not secure so vulnerabilities are discovered. Firewall itself is immune to attack, but “defense in depth” requires

## Slide 235: Internet Security Reviews
User does not understand ramifications of selected firewall architecture (cont.):
    Example 1 (continued): the user insure that every accessible host is secured.
    Example 2: User purchased a proxy based firewall and purchases network scans and scanner sets up the scan on the internal (trusted) network. Reverse of example 1. Vulnerabilities may be found but those hosts are not connected to the internet.

## Slide 236: Internet Security Reviews
User does not understand ramifications of selected firewall architecture (cont.):
  Solution: Read all literature closely. Do not be afraid to ask questions. Think about how IP works and see if there are inconsistencies between what the vendor tells you and what you know about IP. Ask for a detailed explanation of how the firewall handles different types of traffic and problems. Hire a good security consultant if you are not sure. We are available ;)

## Slide 237: The Future
Firewalls will look very different but they will not go away.
  SPEs - Small Protected Enclaves are easier to manage and address specific security needs instead of one size fits all for an entire enterprise.
  Pure Hybrid firewalls
  Secure Applications - Programmers will write secure applications (Pigs will fly and there will be world peace too!)
  IDDs - Intrusion Detection Devices

## Slide 238: Acronyms
CERT - Computer Emergency Response Team
DMZ - De-Militarized Zone
DNS - Domain Name System
FQDN - Fully Qualified Domain Name
FWTK - Firewall Toolkit
InterNIC - Inter Network Information Center

## Slide 239: Acronyms
NS - Name Server
MTA - Mail Transfer Agent
MUA - Mail User Agent
MX - Mail Exchange
RTFM - Read the fine manual.
RFC - Request for Comments
SMTP - Simple Mail Transfer Protocol
SOA - Start of authority

## Slide 240: Troubleshooting Tools
Some tools of the trade:
  dig
  nslookup
  netstat
  ping
  traceroute
  telnet
  tail /var/log/messages

## Slide 241: Where to Get More Information
Other training sessions
Vendors and agencies
Books and Papers
Bug fixes and useful programs

## Slide 242: Other training sessions
Internet Firewalls 101: Theory and Practice
  Marcus J. Ranum, NFR
Building Firewalls: No Theory, Just Practice
  Marcus J. Ranum, NFR
Joining the Internet Safely Using Unix and Firewalls
  Tina Darmohray, iwi
Network Fundamentals for Security Professionals
  Alex Yuriev, Net Access

## Slide 243: Other Training Sessions
Effective Security Incident Response
  Eugene Schultz, SRI
UNIX Security: Threats and Solutions
  Matt Bishop, University of California at Davis
Enterprise Security Solutions
  Alan Paller, SANS Institute
Building A Successful Security Infrastructure
  Michele D. Crabb, Cisco Systems, Inc.

## Slide 244: Vendors
  Secure Networks
  Axent Technologies
  Trusted Information Systems
  Raptor Systems
  Livingston Enterprises
  Cisco Systems

## Slide 245: Books and Papers
RFCs
[RFC819] Su, Z. Postel, J., "The Domain Naming Convention for Internet User Applications." Internet Request For Comment 819 Network Information Center, SRI International, Menlo Park, California. August 1982.
[RFC974] Partridge, C., "Mail Routing and The Domain System." Internet Request For Comment 974 Network Information Center, SRI International, Menlo Park, California. February 1986.

## Slide 246: Books and Papers
RFCs (continued):
[RFC1032] Stahl, M., "Domain Administrators Guide" Internet Request For Comment 1032 Network Information Center, SRI International, Menlo Park, California. November 1987.
[RFC1033] Lottor, M., "Domain Administrators Guide" Internet Request For Comment 1033 Network Information Center, SRI International, Menlo Park, California. November 1987.

## Slide 247: Books and Papers
RFCs (continued):
[RFC1123] R. Braden, Editor, "Requirements for Internet Hosts -- Application and Support" Internet Request For Comment 1123 Network Information Center, SRI International, Menlo Park, California. October 1989.
[RFC1183] Everhart, C., Mamakos, L., Ullmann, R., and Mockapetris, P., "New DNS RR Definitions" Internet Request For Comment 1183 Network Information Center, SRI International, Menlo Park, California. October 1990.

## Slide 248: Books and Papers
RFCs (continued):
[RFC1713] Romao, A., "Tools for DNS debugging" Internet Request For Comment 1713, also FYI27 Network Information Center, SRI International, Menlo Park, California. November 1994.

## Slide 249: Books and Papers
Papers
[Terry] Terry, D. B., Painter, M., Riggle, D. W., and Zhou, S., The Berkeley Internet Name Domain Server. Proceedings USENIX Summer Conference, Salt Lake City, Utah. June 1984, pages 23-31.
[Ranum] Ranum, M., Thinking About Firewalls, SANSII, 1993
[Ranum] Ranum, M., A Toolkit and Methods for Internet Firewalls, ftp.tis.com

## Slide 250: Books and Papers
Papers (continued)
[Zhou] Zhou, S., The Design and Implementation of the Berkeley Internet Name Domain (BIND) Servers. UCB/CSD 84/177. University of California, Berkeley, Computer Science Division. May 1984.

## Slide 251: Books and Papers
Books
[Avolio]Avolio, F., Vixie, P., Sendmail: Theory and Practice, Digital Press, Burlington, MA 1995 ISBN1-55558-127-7.
[Chapman]Chapman, B. & Zwicky, E, Building Internet Firewalls, O’Reilly & Associates, Sebastopol, CA 1995. ISBN 1-56592-124-0.
[Cheswick] Cheswick B. & Bellovin S., Firewalls and Internet Security: Repelling the Wily Hacker, Addison Wesley, New York, 1994. ISBN 0-201-63357-4.

## Slide 252: Books and Papers
Books (continued):
[Comer] Comer, D. Internetworking with TCP/IP Volume I, Prentice Hall, Englewood Cliffs, NJ 1995. ISB 1-56592-127-5.
[Costales]Costales B. with Allman E., sendmail, O’Reilly & Associates, Sebastopol, CA, ISBN-1-56952-056-2.
[Garfinkel] Garfinkel S., Practical Unix & Internet Security, O’Reilly & Associates, Sebastopol, CA, ISBN 1-56592-148-8.

## Slide 253: Books and Papers
Books (continued):
[Hunt] Hunt C., TCP/IP Network Administration, O’Reilly & Associated, Sebastopol, CA, ISBN 0-937175-82-X.
[Liu] Liu, C., Albitz, P., DNS and BIND O'Reilly & Associates, Sebastopol, CA, ISBN 0-937175-82-X 199

## Slide 254: Bug Fixes and Other Useful Info
CERT - www.cert.org
  Firewalls Mailing List
    majordomo@greatcircle.com subscribe firewalls
  Firewall Wizards List
    majordomo@nfr.net subscribe fw-wiz
  Newsgroups
    comp.security.unix
    comp.security.firewalls